## Slide 1: RISC-V AI Accelerator
By roman revzin

## Slide 2: Modules and changes implemented:
Address domain of accelerator increased
  from 0x20 - 0x30 to 0x20 – 0x44
Multiplier module
  Multiplies two 32 bit registers. Output 32 bit as well.
Adder Module
  Summarize two 32 bit registers. Output 32 bit as well.
Mean module
  Calculates mean of the given matrix
Zero mean module
  Shifts expected value of matrix to zero
Variance module
  Calculates variance of the given matrix

## Slide 3: C program
Compiled with gcc 10.1.0:
riscv64-unknown-elf-gcc -Ttext=0 -march=rv32i -mabi=ilp32 test.c -o test & riscv64-unknown-elf-objdump -d test > test.dump & riscv64-unknown-elf-objcopy -O verilog test test.hex --verilog-data-width=4 & .\srec_cat.exe test -binary -o test.mif -mif

## Slide 4: Multiplier
Handles uint8 overflow of output

## Slide 5: Adder
Handles uint8 overflow of output

## Slide 6: Mean
Handles round up

## Slide 7: Zero Mean
Handles uint8 casting of negative values

## Slide 8: Add a Slide Title - 5
Handles round up. Prevents negative values to be zeroed by uint8 casting.

## Slide 9: Performance
All calculations has been performed with combinational circuit, which makes total clock calculation quite complicated.
If we assume propagation delays are negligible compared to the main clock speed, the best performance observed is 6±1 CPU clocks.
Multiple core/thread extension for faster data fetch improve accelerator’s performance significantly.